## Slide 1: Minidrfit Beam Test apply in-lab universal correction
EIC Tracking Meeting
Oct. 27, 2013
B.Azmoun, M.Phipps, BNL

## Slide 2: Compare resolutions from different error functions
Res=141um
Res=110um
Res=104um
Res=141um
Res=125um
Res=108um
Universal Err Fcn
derived from beam
test data
Universal Err Fcn
derived from In-Lab
measurements
Un-corrected
Do not distinguish N-hits
N-hits based correction

## Slide 3: 2Pad Vs 3Pad error functions
The similar N-Pad corrected result implies that the error function is truly universal, especially considering that the measurements taken during the beam test and the in-lab measurements used completely different pad rows on the same readout board.
The differing results from the multi-pad error function (no N-hit discrimination), is due to the fact that the beam test and in-lab measurements had differing N-hit distributions (beam test peaks at 3pad events, in-lab test peaks at 2pad events).
Since the 2-pad and 3-pad error functions are markedly different (below), a multi-pad error function will depend on the ratio of 2pad to 3pad events in the data set from which it is derived.

## Slide 4: Direct Comparison of Error functions
Pink =Beam Test
Blue: In-Lab Test
Beam Test ErrFcn Overlay with 2D residual Vs Centroid
Low statistics, poor ErrFcn
Good Agreement
Poor Agreement

## Slide 5: Conclusions
½ pad N-hit based error function appears to be universal.
N-hit error function yields a better result than a multi-hit error function.
N-hit error functions above 3 hits are not necessary since:
  Events with hits above 3 pads are always low in number (even for angled tracks, since we are only interested in Nhits per time bin, which for a 3cm/us drift velocity, over 25nS, results in a few pads hit at most)
  For Nhits above 3pads, the corresponding error function is not well defined since the response of the readout is derived from several different points along the chevron structure
Apply Error function based on the following method:
  1 pad hit: No correction
  2 pad hit: 2pad universal ErrFcn correction
  3 pad hit: 3pad universal ErrFcn correction
  > 3 pad hit: No correction